## Slide 1
⟶ CLASSIFIED // PROJECT BRIEF ⟵
GLOVE-CONTROLLED
ROBOT
Gesture-Driven 4WD Platform · IMU Sensor Fusion · ESP-NOW Wireless
FLIGHT CREW
ZHANYMKHANOV ALIKHAN
a_zhanymkhanov@kbtu.kz
YESPAN DIAS
d_yespan@kbtu.kz
SAYAN ALISHER
a_sayan@kbtu.kz
SCHOOL OF IT & ENGINEERING · KAZAKH-BRITISH TECHNICAL UNIVERSITY · ALMATY, KAZAKHSTAN

## Slide 2
36TH TFS // GLAMROCK
02 / 10
SECTION 01 // INTRODUCTION
01
MISSION BRIEFING
WHY GESTURE CONTROL · WHY SENSOR FUSION
THE OBJECTIVE
Build a wearable, gesture-driven control interface for a 4WD robotic car — replacing joysticks and buttons with intuitive hand motion.
Hand tilt (pitch / roll) maps directly to FORWARD, BACKWARD, LEFT, RIGHT, STOP commands streamed wirelessly to the robot.
THE CHALLENGE
Each IMU sensor on its own is unreliable:
ACCELEROMETER — noisy under motor vibration (±4° jitter).
GYROSCOPE — drifts over time (~1° per 3 min at rest).
Solution: Kalman-filter sensor fusion + ESP-NOW low-latency wireless.

## Slide 3
36TH TFS // GLAMROCK
03 / 10
SECTION 02 // PRIOR ART
02
PRIOR ART
REFERENCE BASE vs. OUR LOADOUT
Comparison against the reference YouTube build (Arduino-based gesture car):
REFERENCE BASE
MCU — Arduino board
Communication — generic RF
Sensor — accelerometer only
Filtering — none / minimal
Assembly — kit reference build
OUR LOADOUT
MCU — ESP32 (dual-core, Wi-Fi built-in)
Communication — ESP-NOW, ~90 m range
Sensor — MPU6500 (6-axis: accel + gyro)
Filtering — Kalman-filter sensor fusion
Assembly — independent build + custom code

## Slide 4
36TH TFS // GLAMROCK
04 / 10
SECTION 03 // SYSTEM ARCHITECTURE
03
SYSTEM ARCHITECTURE
TWO ESP32 NODES · WIRELESS COMMAND LINK
TX // GLOVE UNIT
MPU6500 IMU
→ 6-axis: accel + gyro, I2C @ GPIO 21/22
ESP32 (transmitter)
→ Read IMU · Kalman fusion · pack & send
Portable battery
→ Glove-side power supply
ESP-NOW
Wi-Fi 2.4 GHz · peer-to-peer
~90 m · < 10 ms latency
RX // ROBOT UNIT
ESP32 (receiver)
→ ESP-NOW callback · decode command
L298N motor driver
→ Dual H-bridge · IN1–IN4 + ENA/ENB PWM
4× DC motors / 4WD chassis
→ Differential drive · powered by 2× 18650

## Slide 5
36TH TFS // GLAMROCK
05 / 10
SECTION 04 // HARDWARE LOADOUT
04
HARDWARE LOADOUT
FIELD-DEPLOYED COMPONENT MANIFEST
# | COMPONENT | SPECIFICATION | ROLE
01 | ESP32 × 2 | Dual-core 240 MHz · Wi-Fi 2.4 GHz · 520 KB SRAM | TX (glove) + RX (robot)
02 | MPU6500 | 6-axis IMU · I2C · 16-bit ADC · ±2–16 g / ±250–2000 °/s | Hand-tilt angle sensing
03 | L298N driver | Dual H-bridge · 2 A / ch · 5–35 V input | Drive 4 DC motors in pairs
04 | DC motors × 4 | Standard 4WD TT motors | Differential drive
05 | 4WD chassis | Plastic frame · motor mounts · wheel axles | Mechanical base
06 | 18650 Li-ion × 2 | 3.7 V nominal · ~2000–3000 mAh · ~7.4 V pack | Boosted to ~14 V for motors
07 | General-purpose PCB | Standard strip / dot board | Soldered robot-side wiring
Glove and robot are powered independently. Robot bus boosted to ~14 V via L298N input; ESP32s run from regulated 3.3 V / 5 V outputs.

## Slide 6
36TH TFS // GLAMROCK
06 / 10
SECTION 05 // SOFTWARE
05
SOFTWARE ARCHITECTURE
TWO FIRMWARES · ONE COMMAND LINK
GLOVE FIRMWARE · TX
Initialize MPU6500 over I2C
Sample accel + gyro at fixed interval Tₛ
Fuse signals with Kalman filter
Compare pitch / roll vs ±30° threshold
Pack command · transmit via ESP-NOW
ROBOT FIRMWARE · RX
Register ESP-NOW receive callback
Decode incoming command packet
Map command → L298N control pins
Set IN1–IN4 logic levels for direction
Apply PWM on ENA / ENB for speed
PSEUDOCODE · ROBOT (RX)
github.com/Absnonsense/Hand_gyro_controller
ON receive(roll, pitch):
IF roll > 25 AND pitch ≈ 0 → MOVE FORWARD
ELIF roll < -25 AND pitch ≈ 0 → MOVE BACKWARD
ELIF pitch < -20 AND roll ≈ 0 → TURN LEFT (reduced PWM)
ELIF pitch > 20 AND roll ≈ 0 → TURN RIGHT (reduced PWM)
ELSE → STOP ALL MOTORS

## Slide 7
36TH TFS // GLAMROCK
07 / 10
SECTION 06 // SENSOR FUSION
06
SENSOR FUSION ENGINE
KALMAN FILTER · ACCEL + GYRO
ACCELEROMETER · NOISY
Trigonometry-based angle is sensitive to vibration. Motor-induced jitter reaches ±4° — unusable for stable control.
GYROSCOPE · DRIFTS
Integration of rotation rate accumulates bias. Stationary signal drifts ~1° over 3 min — unusable long-term.
FUSION LOOP
1 · PREDICT
angle(k) = angle(k−1) + Tₛ · rate(k)
2 · UNCERTAINTY GROWS
P(k) = P(k−1) + Tₛ² · (4°/s)²
3 · KALMAN GAIN
K = P(k) / ( P(k) + 3² )
4 · UPDATE
angle(k) = angle(k) + K · ( accel(k) − angle(k) )
P(k) = (1 − K) · P(k)
K ≈ 1 → trust accelerometer · K ≈ 0 → trust gyroscope

## Slide 8
36TH TFS // GLAMROCK
08 / 10
SECTION 07 // FIELD TEST
07
FIELD TEST RESULTS
VIBRATION · DRIFT · REAL-TIME RESPONSE
FIG 1 · Kalman vs Accelerometer under motor vibration
Chart: Time (s)
Red signal jumps to ±4° once motors start; Kalman output stays near 0°.
FIG 3 · Gyroscope drift over time (rest)
Chart: Time (min)
Gyro climbs to +1° in 3 min while accel stays bounded — motivates fusion.
FIG 2 · REAL-TIME ROLL / PITCH RESPONSE
Hand tilted laterally at sample ≈5421 → Roll spikes from ~0° to ~18° while Pitch stays flat. Axes decoupled correctly; gesture detection logic validated in real time.

## Slide 9
36TH TFS // GLAMROCK
09 / 10
SECTION 08 // PERFORMANCE
08
PERFORMANCE METRICS
GESTURE TABLE · WIRELESS LINK
~90 m
OPEN-SPACE RANGE
< 10 ms
COMMAND LATENCY
±30°
DEAD-ZONE GATE
5 / 5
GESTURES CONSISTENT
GESTURE COMMAND TABLE
GESTURE | AXIS | THRESHOLD | COMMAND | RESPONSE
Forward tilt | Pitch | > +30° | MOVE FORWARD | Consistent
Backward tilt | Pitch | < −30° | MOVE BACKWARD | Consistent
Left tilt | Roll | < −30° | TURN LEFT | Consistent
Right tilt | Roll | > +30° | TURN RIGHT | Consistent
Neutral | Both | within ±30° | STOP | Consistent

## Slide 10
36TH TFS // GLAMROCK
10 / 10
SECTION 09 // DEBRIEF
09
MISSION DEBRIEF
CONCLUSION · FUTURE OPS · END OF BRIEFING
CONCLUSION
Glove-controlled 4WD robot fully operational.
Kalman fusion suppressed motor-vibration noise and gyro drift.
ESP-NOW link delivered low-latency control at ~90 m.
All five gesture commands triggered consistently.
Low-cost, responsive HRI platform for education and research.
FUTURE OPS
Variable speed proportional to tilt magnitude.
Expanded gesture vocabulary (rotation, fist, etc.).
Robot → glove feedback (battery, obstacles) over the bidirectional link.
Onboard camera for FPV / object tracking.
Haptic feedback in glove (vibration on impact).
END OF BRIEFING · QUESTIONS?
36TH TFS // GLAMROCK